Steller’s Jay aversion conditioning Treatment

In the Santa Cruz Mountains In 2013

Prepared and submitted by

Pia O. Gabriel1,2, Portia Halbert3, and Richard T. Golightly1,2

1Humboldt State University

2H. T. Harvey & Associates

3California State Parks

February 2014

Report to COSCO BUSAN Trustee Council

Steller’s Jay Conditioned Aversion Treatment

In the Santa Cruz Mountains In 2013

Pia Gabriel1,2, Portia Halbert3, and Richard Golightly1,2

1Humboldt State University, Wildlife Department, 1 Harpst Street, Arcata CA 95521

2H. T. Harvey & Associates, Ecological Consultants, 1125 16th Street, Arcata CA 95521

3California State Parks, 303 Big Trees Park Road, Felton CA 95018

Introduction

Predation on eggs of marbled murrelets (Brachyramphus marmoratus) has been linked to poor recruitment of young into the murrelet population, especially in the California, Oregon and Washington populations (McShane et al. 2004, Hébert and Golightly 2007, Golightly and Schneider 2009, Peery and Henry 2010). Corvids have been implicated as the most influential egg predators on murrelets. Fragmented forests provide the only remaining murrelet nesting habitat in California; unfortunately, these forests also support great densities of opportunistic corvids like Steller’s jays (Cyanocitta stelleri), increasing predation risk on murrelet eggs (Marzluff et al. 2004, Marzluff and Neatherlin 2006, Golightly and Gabriel 2009, Malt and Lank 2009). Effective reductions of egg predation require manipulation of the predator population density or predation behavior.

Conditioned aversion techniques for Steller’s jays that exposed the jays to murrelet-colored and sized eggs treated with carbachol (carbamylcholine chloride) effectively induced subsequent aversion to the murrelet-mimic eggs in laboratory and field tests (Gabriel and Golightly 2011). Implementation of the technique in the Santa Cruz mountains in 2012, where carbachol-laced murrelet-mimic eggs were deployed at densities of 0.5 – 2 eggs / ha, reduced corvid predation on murrelet-mimic eggs by 44% to 80% (Gabriel and Golightly 2011, Gabriel et al. 2013). Peery and Henry (2010) calculated that reductions in corvid predation on murrelet nests between 40 and 70% (depending on a range of assumptions regarding nesting ratios and predation rates) would be necessary to stabilize the imperiled marbled murrelet population segment located in central California.

In the first deployment of 2012 in the Santa Cruz mountains, 49 % of murrelet-mimic eggs were unpredated. This implied that the deployment density of eggs may have been much greater than necessary and resulted in many jays encountering more than one treated murrelet-mimic eggs within their territories. Thus estimates of predation reduction derived from this implementation probably underestimated the potential for conditioned aversion, and treatment would be expected to be effective at lower egg densities. To continue improving reproductive success of murrelets in central California, conditioned aversion was again applied as a management technique in Butano State Park and Portola Redwoods State Park in spring 2013. In addition, the treatment area was expanded to include campgrounds at Memorial County Park. Although we expected lower egg densities to be effective in treating jays, treatment densities were maintained at comparable levels to 2012 to allow direct comparison between the effectiveness of deployments in both years. In particular, comparable deployment densities allowed assessment of possible carry-over of conditioned aversion, where jays that were treated in 2012 and were still resident in the treatment areas in 2013 would be expected to still avoid mimic eggs in 2013.

Methods

Conditioned aversion treatment was focused on approximately 650 ha of forested areas surrounding high-visitor use areas of Butano State Park, Portola Redwoods State Park, and Memorial County Park in San Mateo County in spring 2013. These areas were identified among the habitat important to murrelet recovery and currently occupied by murrelets in central California by the U.S. Fish and Wildlife Service (USFWS 2008). Treatment consisted of deployment of carbachol-laced eggs that mimicked murrelet eggs in contiguous habitat used by jays in old growth or second growth forest stands around campgrounds. In Butano and Portola Redwoods State Parks, conditioned aversion treatment had previously been applied to approximately 600 ha in 2012 (Gabriel et al. 2013). The treatment area in 2013 overlapped the 2012 deployment area in these parks by approximately 80%, where some areas that received deployments in 2012 did not in 2013, and some areas were treated for the first time in 2013.

Deployment areas were based on reports that anthropogenic habitat alteration and food supplementation had affected jay populations within 1 to 2 km of high-use visitor attractions (W. Goldenberg, L. George, J. Black, and E. Doucet-Beer, Z. Peery, unpublished data). Furthermore, the forests surrounding the parks and campgrounds that were the focus of treatment were very fragmented, and thus very attractive to populations of Steller’s jays. We used the rationale that, instead of merely treating islands of murrelet breeding habitat, edges between murrelet breeding habitat and surrounding forest were particularly important for also treating jays that may be predating murrelet nests (Marzluff et al. 2004, Malt and Lank 2009).

Egg preparation

Laboratory preparation of treatment eggs began in February using raw, small-sized chicken eggs that weighed 42 to 45 g. A small hole of approximately 3 mm diameter was drilled in the narrowest end of the shell using a rotary tool. We extracted 0.5 to 1 ml of egg contents with a syringe to provide for the subsequent addition of aversive chemical solution and for expansion of egg contents with temperature. We then injected at least 0.24 ml of a sterile solution containing 100 mg/ml carbachol (carbamylcholine chloride, 99%, Acros Organics, Thermo Fisher Scientific, New Jersey, U.S.A; approximately 0.7 mg carbachol / g egg mass). A piece of wire approximately 2 mm in diameter, with the tip bent at an approximate angle of 10° and attached to a rotary tool was inserted into the drilled hole. The rotary tool was activated for 1 to 2 s, resulting in a short burst of whisking to thoroughly blend the contents of the egg with the carbachol solution. The egg surface was then wiped clean and the hole sealed with hot glue (Dualmelt G GS25DT, Stanley Tools, Connecticut, U.S.A.).

Eggs were colored with paint in a blue-green hue closely resembling murrelet eggs (Oceanfront 660, Benjamin Moore & Co., New Jersey, U.S.A.) using a spray can. Irregular black spotting as displayed on murrelet eggs was applied with dilute acrylic paint. An approximately 1 cm2 piece of double sided hook-and-loop fastener (Velcro brand) was then attached with hot glue to all eggs along 2 cm of their widest side. A matching piece of hook-and-loop fastener was glued to a 20 cm black zip tie (8” x 3/16” Black Nylon Cable Tie; Storehouse, Harbor Freight Tools, Camarillo, California, U.S.A.). This provided a flexible attachment that allowed us to fasten eggs to tree branches with the zip tie.

Field deployment

Three temporally distinct deployments of treatment eggs were implemented. Jay territories largely overlap among mates and to varying degrees among neighbors (Brown 1963), and predation by rodents may have previously caused some loss of treatment eggs. Consequently, some jays may not have been exposed to eggs in the first deployment. The goal of a second deployment was to maximize the number of jays exposed to treatment eggs. The purpose of the third deployment, applied in late spring when the jay population included many newly fledged jays, was to assess the predation impact of previously untreated juvenile jays. The first field deployment was conducted between 4 March and 29 April, the second treatment between 11 March and 22 May, and the third treatment between 2 April and 13 June 2013. Removal of egg remains and egg-attachment materials occurred between 5 May and 25 June 2013. Although logistical considerations resulted in temporal overlap among deployment periods, successive deployments in any single location were always dicrete, and never overlapping.

Treatment eggs were placed at intervals of 100 m along roads and trails throughout the parks in the areas surrounding high-use visitor attractions. Eggs were placed in trees that provided a branch suitable for placing an egg in the sub-canopy, between 3 and 5 m height above ground. Given the great density of trails surrounding high-visitor use areas in the central California parks, treatment density approximated between 0.5 to 2 treatment eggs / ha. The use of roads and trails for egg deployment resulted in the greatest treatment densities in areas with greatest density of human development, and coincided with greatest expected jay densities (Bensen 2008, Suddjian 2009). In the first deployment, 313 treated eggs were placed in Butano State Park, 183 treated eggs were placed in Portola Redwoods State Park, and 15 treated eggs were placed in Memorial County Park (Fig. 1).

During the second deployment of treated eggs, the disposition of eggs placed during the first deployment was determined. This resulted in intervals of 3 to 36 days between the first deployment and assessment of egg predation. During the third deployment of treated eggs, the disposition of eggs placed during the second deployment was determined. This resulted in intervals of 7 to 43 days between the first deployment and assessment of egg predation. During the removal of remains after the third deployment, the disposition of eggs placed during the third deployment was determined. This resulted in intervals of 3 to 62 days between the third deployment and assessment of egg predation. Disposition of eggs was scored in three categories based on visible signs of predation (Table 1).

Table 1. Predation categories assigned to eggs after first, second, and third deployments of carbachol-treated murrelet-mimic eggs in central California parks for aversive conditioning of wild Steller’s Jays.

| Predation category | Description of egg disposition |
| --- | --- |
| No predation | Egg was intact |
| Possible corvid predation | Egg showed sign of unknown predator, or egg missing |
| Corvid predation | Egg remains showed conclusive signs of corvid attack |
| Unknown | Eggs or egg remains were found, but not enough evidence collected to assign predation categorya |

aIntact eggs (no predation) could almost always, and missing eggs (possible corvid predation) could always be unambiguously assigned; thus proportions of assigned predation classes overrepresent the category ‘no predation’, probably underrepresent the category ‘possible corvid predation’, and most strongly underrepresent the category ‘corvid predation’.

We assessed whether jays in Butano and Portola Redwoods State Park retained aversions acquired by exposure to treatment in 2012 by comparing the proportion of mimic eggs that remained unpredated in the first deployment of 2013 to the two deployments of 2012. Since considerably larger proportions of predated eggs could not be assessed for corvid predation reliably or within a suitable time frame in 2012 than in 2013, the proportion of eggs remaining unpredated was the most reliable metric that could be directly compared between deployments in the two different years.

The effectiveness of aversive conditioning in protecting murrelet-mimic eggs from predation in 2013 was determined by comparing the predation rate of murrelet-mimic eggs between the first, second, and third egg deployments in Butano and Portola Redwoods State Parks. First we compared the overall proportions of predated mimic eggs in the two deployments. Second we compared the proportions of predation on mimic eggs located in or close to campgrounds within the treatment area to the remainder of the treatment area. We used Chi-square tests to compare proportions of mimic eggs in each predation category (not predated, possibly corvid predated, and corvid predated). When significant differences in these proportions between the respective sets of eggs (first deployment compared to second deployment, or within campgrounds compared to outside campgrounds, or close to campgrounds compared to away from campgrounds) were found, we then used two different groupings of predation categories for more detailed comparisons; for a maximally inclusive measure of corvid predation, eggs that were categorized as possibly corvid predated and as corvid predated were added together and compared to eggs that were not predated; for a maximally stringent measure of corvid predation only eggs that were categorized as corvid predated were used and contrasted to eggs that were not predated, and in this sense eggs categorized as possibly corvid predated were excluded from comparisons. Where contingency tables contained expected counts below 5 in any category, we used Fisher’s exact test (for 2x2 tables) or Monte Carlo simulations with 10,000 iterations to estimate Chi-Square and P-values (for larger tables).

We examined whether proportions of predation categories differed between the first deployment and the second deployment. We included only locations that had been revisited 14 to 35 days after deployment, or if the egg was found intact (not predated) any time after 14 days; these criteria were comparable to the time interval that was found to be suitable for correct classification of predation in the field assessment of aversion conditioning effectiveness on jays in Redwood National Park (Gabriel & Golightly 2011), and correspond to criteria used for equivalent analyses of predation data collected in the same parks in 2012 (Gabriel et al. 2013). Note that under this set of criteria, unpredated eggs were slightly overrepresented relative to a direct count of eggs scored for each predation category. The imbalance among predation categories influenced interpretation of the absolute distribution of predation categories, but not the relative change between subsequent deployments.

Utilization of data collected only within 14 to 35 days after each deployment resulted in inadequate sample sizes for spatial analyses. We therefore repeated the examination whether proportions of predation scores differed between the first deployment and the second deployment under less rigorous criteria where all egg locations were included that could be classified as not predated, possibly corvid predated, or corvid predated (see Table 1). This second set of analyses allowed direct comparison of changes in overall predation between the first and second deployment with spatial distributions of predation in and outside of campgrounds. Under these criteria, unpredated eggs were also slightly overrepresented relative to the other two predation categories (for details see Table 1).

We assessed whether effectiveness of conditioned aversion treatment and adequacy of deployment density differed between campgrounds and areas outside of campgrounds. For this purpose we compared proportions of predation categories between egg locations in campgrounds to locations outside campgrounds (Fig. 1) in the first deployment, second deployment, and third deployment. Using an estimated 1 km radius of anthropogenic effects of campgrounds on jay populations (W. Goldenberg, L. George, and J. Black, unpublished data), we also compared proportions of predation categories between egg locations within 1 km of campgrounds to egg locations more than 1 km away from campgrounds (Fig. 1). Because of sample size limitations, no selection criteria regarding revisitation intervals were applied to the data for these analyses; instead all egg locations were included that could be assigned with a predation category (not predated, possibly corvid predated, or corvid predated; see Table 1).

Figure 1. Deployment locations of murrelet-mimic eggs in campgrounds (gray circles), within 1km of campgrounds (black circles), and more than 1 km away from campgrounds (white circles) in Butano State Park, Portola Redwoods State Park, and Memorial County Park, California.

We also monitored interactions of corvids and other species with treated eggs with infra-red motion sensor cameras (Trophy Cam Trail Camera, Bushnell Outdoor Products, Kansas, U.S.A.). Cameras were placed at egg locations distributed throughout the deployment area and visited approximately once a week. Four cameras were placed at 12 different egg locations in Portola Redwoods State Park. Four other cameras were placed in 14 different locations in Butano State Park, and three other cameras were placed at 9 different locations in Memorial County Park. Once a camera-monitored egg was predated, the camera was moved to new location. If predation by a non-corvid predator was suspected, the immediate surroundings of the tree were searched for any animals or sign of animals. Photos obtained from trail cameras allowed identification of predators and behavioral evaluation of animal interactions with treated eggs.

Results

At Butano State Park and Portola Redwoods State Park, corvid predation in the first egg deployment could be assessed at all revisited egg locations, and 63% of all locations after the first deployment were not predated. In the second field deployment, 68% of revisited egg locations were not predated, while 1% of locations could not be assessed for corvid predation. In the third field deployment, 70% of revisited egg locations were not predated, while 0.7% of locations could not be assessed for corvid predation (Table 2). Eggs that could not be assigned with a predation category were excluded from further analyses. In comparison to eggs deployed in the same two parks in 2012, the percentage of unpredated eggs in the first egg deployment of 2013 was 29% higher than in the first egg deployment of 2012 (Χ21 = 20.74, P < 0.001; Fig. 2), but was similar to the percentage of unpredated eggs in the second deployment of 2012 (Χ21 = 1.88, P = 0.171; Fig. 2).

At Memorial County Park, 15 eggs were revisited after the first deployment, and 53% were not predated. In the second field deployment, 12 eggs were revisited and 17% were not predated (Table 2). Egg locations at Memorial County Park were not included in further comparisons.

Table 2. Disposition of eggs after first (1st), second (2nd), and third (3rd) egg deployments of murrelet-mimic eggs in Butano State Park, Portola Redwoods State Park, and Memorial County Park. Number of eggs shown when including predation categories for all eggs assigned according to Table 1 anytime during entire assessment period, and when including only eggs revisited 14 to 35 days after deployment or if the egg was found intact any time after 14 days.

| Predation outcome |  | Disposition over entire period |  | Disposition 14-35 days after deployment |
| --- | --- | --- | --- | --- |
|  |  | 1st | 2nd | 3rd |  | 1st | 2nd | 3rd |
| Butano & Portola Redwoods State Parks |  |  |  |  |  |  |  |  |
| Predated by corvid |  | 51 | 16 | 15 |  | 44 | 14 | 11 |
| Possibly predated by corvid |  | 133 | 135 | 99 |  | 119 | 111 | 97 |
| Not predated |  | 310 | 331 | 267 |  | 305 | 330 | 265 |
| Total eggs with valid predation score |  | 494 | 482 | 381 |  | 468 | 455 | 373 |
| Total eggs excluded by criteria |  | 0 | 7 | 3 |  | 26 | 34 | 11 |
| Total eggs revisited |  | 494 | 489 | 384 |  | 494 | 489 | 384 |
| Memorial County Park |  |  |  |  |  |  |  |  |
| Predated by corvid |  | 1 | 1 |  |  | 1 | 1 |  |
| Possibly predated by corvid |  | 6 | 9 |  |  | 6 | 9 |  |
| Not predated |  | 8 | 2 |  |  | 8 | 2 |  |

Figure 2. Proportion of all revisited egg locations where eggs were found intact after first (n = 527), and second deployments (n = 484) of murrelet-mimic eggs in Butano State Park and Portola Redwoods State Park in 2012, and after first (n = 494), second (n = 489), and third deployments (n = 384) in the same two parks in 2013.

Trail cameras acquired 361 pictures of eight different wildlife species interacting with or moving in close vicinity of mimic eggs. Series of photographs that were acquired within 10 minutes of each other at the same location likely depicted the same individual animal and were interpreted cumulatively as single interactions. According to these criteria, we identified 55 unique wildlife interactions. Many interactions involved the same species at the same location or nearby locations that may have been in close enough proximity to be included in the same home range. The 55 unique interactions may therefore have included multiple recorded interactions of the same individual animals. Nineteen (35%) of these interactions were Steller’s jays (Fig 3). We acquired 20 interactions of western gray squirrels (Sciurus griseus), 16 of which were recorded at the same location where the same individual appeared to travel periodically along the tree, possibly to and from its nest in the canopy (Fig. 4a). We also recorded two interactions of gray foxes (Urocyon cinereoargenteus; Fig. 4b), one chipmunk (Neotamias spec. Fig. 4c), three unknown mice (Fig. 4d), eight unknown mammals, one American robin (Turdus migratorius), and one unknown bird.

Figure 3. Photographs acquired by trail cameras in central California parks showing Steller’s jays in the vicinity of carbachol-laced murrelet-mimic eggs.

Figure 4. Photographs acquired by trail cameras in central California parks showing one squirrel (a), one grey fox (b), one chipmunk (c) and one mouse (d) in the vicinity of carbachol-laced murrelet-mimic eggs.

Aversive conditioning effects including only eggs revisited after 14 to 35 days

In 2013 at Butano and Portola Redwood State parks, the distribution of predation categories differed among the three deployments (Χ22 = 25.10, P < 0.001, Fig. 5). Using maximally inclusive measures (possibly corvid predated and corvid predated eggs combined, see Fig. 5), the proportion of murrelet-mimic eggs predated in the second deployment was 21% less than in the first deployment (Χ21 = 5.82, P = 0.016), but the proportion of predated murrelet-mimic eggs did not differ between the second and third deployments (Χ21 = 0.22, P = 0.637). Using maximally stringent measures (only corvid predated eggs included, see Fig. 5), the proportion of murrelet-mimic eggs predated in the second deployment was 68% less than in the first deployment (Χ21= 16.47, P < 0.001), but the proportion of predated murrelet-mimic eggs did not differ between the second and third deployments (Χ21 < 0.01, P = 0.958).

Figure 5. Proportion of eggs in three disposition categories, excluding unknown disposition, and assessed within 14 to 35 days after deployments, or if unpredated any time after 14 days, after first (n = 468), second (n = 455), and third deployments (n = 373) of murrelet-mimic eggs in Butano State Park and Portola Redwoods State Park. Predation categories are described in Table 1.

Aversive conditioning effects including all eggs with assigned predation scores

In 2013 at Butano and Portola Redwood State Parks, the distribution of predation categories differed among the three deployments (Χ22 = 26.09, P < 0.001; Fig. 6). Using maximally inclusive measures, the proportion of murrelet-mimic eggs predated in the second deployment was 16% less than in the first deployment, but the difference was not significant (Χ21 = 3.79, P = 0.052). The proportion of predated murrelet-mimic eggs did not differ between the second and third deployments (Χ21 = 0.20, P = 0.656). Using maximally stringent measures, the proportion of murrelet-mimic eggs predated in the second deployment was 67% less than in the first deployment (Χ21 = 18.70, P < 0.001, Fig. 6), but the proportion of predated murrelet-mimic eggs did not differ between the second and third deployments (Χ21 = 0.167, P = 0.68; Fig. 6).

Figure 6. Proportion of eggs in three disposition categories, excluding unknown disposition, after first (n = 494), second (n = 482), and third deployments (n = 381) of murrelet-mimic eggs in Butano State Park and Portola Redwoods State Park. Predation categories are described in Table 1.

Comparisons between egg locations relative to campgrounds

In the first deployment, the distribution of predation categories differed between egg locations in campgrounds and locations outside of campgrounds (Χ22 = 25.96, P < 0.001, Fig. 7). Using maximally inclusive measures (possibly corvid predated and corvid predated eggs combined, see Fig. 9), the proportion of murrelet-mimic eggs predated in campgrounds was 126% greater than outside of campgrounds (Fisher’s exact test, P < 0.001). Using maximally stringent measures (only corvid predated eggs included, see Fig. 7) the proportion of murrelet-mimic eggs predated in campgrounds was 396% greater than outside of campgrounds (Fisher’s exact test, P < 0.001). In the second deployment, the distribution of predation scores also differed between egg locations in campgrounds and locations outside of campgrounds (Χ22 = 10.65, P = 0.013, Fig. 7). However, using maximally inclusive measures, the proportion of predated murrelet-mimic eggs did not differ between locations in and outside of campgrounds (Fisher’s exact test, P = 0.301). Using maximally stringent measures, the proportion of murrelet-mimic eggs predated in campgrounds was 416% greater than outside of campgrounds (Fisher’s exact test, P = 0.011). In the third deployment, the distribution of predation categories did not differ between egg locations in campgrounds and locations outside of campgrounds (Χ22 = 3.00, P = 0.246, Fig. 7).

Figure 7. Proportion of eggs in three disposition categories, excluding unknown disposition, after first, second, and third deployments of murrelet-mimic eggs in campgrounds (Camp) and outside of campgrounds (No camp) in Butano State Park and Portola Redwoods State Park. Sample sizes shown inside bars. Predation categories are described in Table 1.

When assessing effects of campgrounds on jay populations surrounding these campgrounds, the distribution of predation categories did not differ between egg locations within 1 km of campgrounds and locations more than 1 km away from campgrounds in any of the three deployments (Χ22 = 0.61 - 1.60, P = 0.449 – 0.737; Fig. 8).

Figure 8. Proportion of eggs in three disposition categories, excluding unknown disposition, after first, second, and third deployments of murrelet-mimic eggs within 1 km of campgrounds (< 1 km) and more than 1 km away from campgrounds (> 1 km) in Butano State Park and Portola Redwoods State Park. Sample sizes shown inside bars. Predation categories are described in Table 1.

Discussion

Deployment of murrelet-mimic eggs laced with carbachol for a second consecutive year in the forests surrounding high-visitor use areas of Butano State Park and Portola Redwoods State Park was effective at reducing predation by Steller’s jays on the murrelet-mimic eggs. Moreover, the initial predation rate on murrelet-mimic eggs in 2013 was similar to the predation rate after conditioning in 2012, suggesting a possible carry-over effect of conditioned aversion, where many jays that were treated in 2012 may still have retained their avoidance of mimic eggs in 2013.

The effectiveness of aversion achieved by the conditioning in 2013 was somewhat lower than in 2012 (Gabriel et al. 2013). Using the most rigorous analysis criteria (14 to 35 day egg revisitation and assessment interval) and maximally inclusive assumptions (where all possible corvid predation was included in comparisons), we detected a decrease in predation of 21% between the first and second deployments in 2013, compared to a 44% decrease in 2012. Maximally stringent assumptions (where possible corvid predation was excluded from comparisons) suggested a predation decrease of 68%, compared to an 80% decrease in 2012. This lesser relative effect of treatment was unsurprising in context with an already significantly lower initial predation rate in 2013 compared to 2012, especially if this difference resulted from retention of aversive conditioning already achieved in 2012. The carry-over effect between years was not complete, as was evident by the additional reduction in predation rates between the first and second deployment in 2013. Approximately 45 deployment locations in 2013 were in areas where no mimic eggs were deployed in 2012, and therefore likely included jay territories that had received no previous conditioning treatment. Moreover, some jays fledged in summer 2012 and some jays previously living in adjacent untreated areas likely either immigrated into treated areas to replace previous residents that died between the 2012 and 2013 deployments, or shifted home range boundaries (Gabriel 2012). Also, many jays fledged in summer 2012 were likely unsuccessful in establishing a breeding territory in spring 2013, but instead prospected over a large area (Goldenberg 2013). All of these conditions likely contributed to some jays encountering treated eggs for the first time in 2013. Due to large individual behavioral differences that exist within jay populations, including for foraging behaviors (Gabriel and Golightly 2011; Rockwell et al. 2012, 2013), it is also possible that individual jays differ in the retention of conditioned aversions, where some individuals may not have retained an aversion acquired in 2012 for an entire year.

Predation rates on mimic eggs did not change significantly between the second and third deployments in 2013. This may suggest that most egg predating jays in the deployment area were successfully treated in the first deployment, and no significant additional conditioning was achieved by the second deployment. However, the third deployment was carried out in late spring when the jay population included many newly fledged jays. The addition of these previously untreated jays could be expected to result in increased predation rates on mimic eggs. The absence of an increase in predation rates in the third deployment may indicate either that predation by juveniles was negligible, or that increased predation by juvenile jays was offset by potential additional conditioning of adult jays achieved by the second deployment. Without the use of control eggs, the current data does not allow us to distinguish between these two alternative explanations. However, the consumption of eggs is a relatively complex foraging behavior that appears to be successfully learned only by a subset of the jay population (Gabriel and Golightly 2011). Juvenile jays may largely lack the experience to successfully predate eggs, especially if they do not have the opportunity to learn by example from parents and other adult conspecifics (Templeton et al. 1999; Midford et al. 2000) because those adults have been conditioned to avoid eggs. Juveniles without the opportunity for social learning of egg predation may therefore be less likely to predate eggs as adults. If this is the case, the proportional carry-over effect of conditioning may be expected to increase over time, as the proportion of egg predating individuals would decrease in the adult, resident jay population.

In contrast to 2012, the proximity to campgrounds (within or outside 1 km) did not influence the likelihood of mimic eggs to be predated in 2013. In the first deployment of 2012, the majority of unpredated mimic eggs in the first deployment were located within 1 km of campgrounds. We attributed this to jays living within 1 km of campgrounds encountering multiple egg pairs within their territory much more often, and subsequently avoiding eggs because they had already been conditioned on the next encounter, because deployment density was about twice than in locations outside of 1 km of campgrounds (Gabriel et al. 2013). In the second deployment of 2012, the proportion of unpredated eggs outside of 1 km of campgrounds had risen to similar levels as within 1 km of campgrounds, presumably due to successful treatment. In 2013, the proportion of unpredated mimic eggs in areas both within and outside 1 km of campgrounds was similar and also comparable to unpredated proportions in both these areas in the second deployment of 2012. This supports the interpretation that in 2013, jays throughout the deployment area retained egg aversions acquired by the conditioning treatment applied in 2012.

During the first and second deployments of 2013, proportionally more eggs were predated within campgrounds than outside of campground boundaries. Comparison with the predation patterns in relation to campgrounds in 2012 suggests that the carry-over effect of conditioning was strong outside of campgrounds, with close to 70% of mimic eggs remaining unpredated in the second deployment of 2012 and again in the first deployment of 2013. By contrast, predation within campgrounds shows a marked increase between the second deployment of 2012 and the first deployment of 2013. This suggests that the great majority of new, untrained jays that were presumably responsible for much of the predation on mimic eggs in campgrounds were immigrants attracted by anthropogenic food directly into the campgrounds, whereas the treated jay populations outside campgrounds remained relatively stable between the two years. It is important to note that due to the comparatively small area and resulting small number of eggs deployed within campgrounds, a relatively small number of individual jays can produce a large proportional change in predation rates measured within these campgrounds. Campgrounds in the central California parks opened for visitors between 1 March and 1 April. Thus the elevated egg predation in the campgrounds in the first and second deployments of 2013 coincided with a large increase in the availability of anthropogenic food, equivalent to the second deployment of 2012 during which egg predation in campgrounds was also elevated. Jay parents travelling with young fledglings, as well as second-year birds without breeding territories may travel longer distances than territorial jays during the breeding season and aggregate at profitable food sources such as campgrounds (Gabriel & Black 2008; Goldenberg 2013). Thus, jays predating mimic eggs in campgrounds during the first and second deployments of 2013 likely encountered mimic eggs for the first time. Thus we re-iterate our recommendation that retaining the use of a second deployment into the future to complete the exposure of temporally and spatially distributed corvids living throughout the parks and adjacent lands seems prudent.

Data from trail camera pictures in 2013, similar to data from 2012, suggested that loss of mimic-eggs to non-corvid wildlife was minimal. Although 65% of the 55 wildlife interactions recorded showed non-corvids, the great majority of the pictures documented small mammals moving in the vicinity without any direct interaction with the mimic eggs, many simply travelling repeatedly along the tree holding the mimic egg. The only conclusive photographic evidence of direct predation by a non-corvid was one photo series showing predation by a grey fox. In addition, although comparable overall numbers of wildlife interactions were captured in the two years (51 total interactions in 2012), the number of interactions by Steller’s jays had dropped to less than half in 2013, with 19 jay interactions in 2013 compared to 45 in 2012. This may confirm the interpretation of a successful carry-over effect of conditioned aversion, where many jays that were treated in 2012 still avoided mimic eggs in 2013. Several photo series showed juvenile jays inspecting and attempting to manipulate mimic eggs, often for long periods of time, but never successfully opening and predating eggs. These observations may support the assumption that juvenile jays largely lack the experience to predate eggs without the opportunity to learn from experienced adults.

Management Recommendations

This second consecutive large field treatment in central California confirmed that behavioral training of Steller’s jays to avoid murrelet-mimic eggs was possible over large landscapes. The conditioning effect achieved in the first year of deployment carried over to a large extent to the second year. Retention of the aversion acquired in the first year into the second year appeared virtually complete in deployment areas outside of campgrounds, implying that jay populations remained mostly stable in forests away from campgrounds. Therefore, reducing the frequency to one set of deployments every two years may have similar efficiency as annual deployments in forest areas away from campgrounds. By contrast, deployment areas within campgrounds appeared to attract the majority of untreated immigrants, negating any carry-over effect from aversive treatments in the previous year in these small, but densely populated areas. Most new visitors to the campgrounds were likely second-year birds prospecting for nearby breeding territories, or adults from nearby established territories travelling with fledged young. Thus, continuation of annual deployments within campgrounds may achieve continuous protection of murrelet nests within as well as adjacent to campgrounds.

Acknowledgments

This research was funded by the COSCO BUSAN Oil Spill Restoration Fund and administered by California State Parks. We are particularly indebted to the Office of Spill Prevention and Response, California Department of Fish and Game for their consideration of testing novel approaches to improve Marbled Murrelet nesting habitat, especially Dr. S. Hampton. We also thank C. Marn, J. Whitlock and L. Roberts of U.S. Fish and Wildlife Service and J. Boyce of the National Oceanic and Atmospheric Administration for facilitating the project. H. Ernst steered field efforts and provided valuable assistance with data evaluation. The study was conducted under Humboldt State University’s Institutional Animal Care and Use Protocol No. 10/11.W.41.A.

References

Bensen, K.J. 2008. Forest and beach corvid monitoring and management, Redwood Creek corvid and backcountry campsite mapping, trail and backcountry management plan implementation – 2008 progress report. National Park Service, Redwood National and State Parks, Orick, CA.

Brown, J. 1963. Aggressiveness, dominance and social organization of the Steller’s jay. Condor 65: 460-484.

Gabriel, P.O., and J.M. Black. 2008. Seasonal habitat use by urban Steller’s jays. The Western Section of the Wildlife Society Conference. Redding, California, February 2008.

Gabriel, P.O., and R.T. Golightly. 2011. Experimental assessment of taste aversion conditioning on Steller’s Jays to provide potential short-term improvement of nest survival of Marbled Murrelets in northern California. Report submitted to National Park Service, Orick, CA. 34 pp.

Gabriel, P.O., P. Halbert, and R.T. Golightly. 2013. Steller’s jay conditioned taste aversion treatment in the Santa Cruz mountains in 2012. Report submitted to COSCO BUSAN Trustee Council, California Department of Fish and Game, Office for Oil Spill Prevention and Response, Sacramento, CA.

Goldenberg, W.P. 2013. Steller’s jay space use and behavior in campground and non-campground sites within Redwood National and State Parks. Masters Thesis. Humboldt State University, Arcata, CA.

Golightly, R.T., and P.O. Gabriel. 2009. Marbled Murrelets. Pp. 65-106 In Colwell, M.A., T.L. George, and R.T. Golightly [eds.].  A predator management strategy to address corvid impacts on productivity of Snowy Plovers (Charadrius alexandrinus) and Marbled Murrelets (Brachyramphus marmoratus) in coastal northern California. Final Report submitted to U.S. Fish and Wildlife Service, Arcata, CA. 115 pp.

Golightly, R.T., and S.R. Schneider. 2009. Observations of incubation in year 8 of a long-term monitoring effort at a marbled murrelet nest in northern California. Report to the California Department of Fish and Game, Sacramento, CA. 37 pp.

Greene, E., W. Davison, and V.R. Muehter.1998. Steller’s Jay (Cyanocitta stelleri). Account 343 In Poole, A., and F. Gill [eds.]. The Birds of North America. The Academy of Natural Sciences, Philadelphia, Pennsylvania, and The American Ornithologists’ Union, Washington D.C., USA.

Hébert, P.N., and R.T. Golightly. 2007. Observations of predation by corvids at a Marbled Murrelet nest. Journal of Field Ornithology 78: 221-224.

Malt, J.M., and D.B. Lank. 2009. Marbled murrelet nest predation risk in managed forest landscapes: dynamic fragmentation effects at multiple scales. Ecological Applications 19: 1274-1287.

Marzluff, J.M., J.J. Millspaugh, P. Hurvitz, and M.S. Handcock. 2004. Relating resources to a probabilistic measure of space use: forest fragments and Steller’s jays. Ecology 85: 1411-1427.

Marzluff, J.M., and E. Neatherlin. 2006. Corvid response to human settlements and campgrounds: Causes, consequences, and challenges for conservation. Biological Conservation 130: 301-314.

McShane, C., T. Hamer, H. Carter, G. Swartzman, V. Friesen, D. Ainley, R. Tressler, K. Nelson, A. Burger, L. Spear, T. Mohagen, R. Martin, L. Henkel, K. Prindle, C. Strong, and J. Keany. 2004. Evaluation report for the 5-year status review of the marbled murrelet in Washington, Oregon, and California. Unpublished report. EDAW, Inc. Seattle, Washington. Prepared for the U.S. Fish and Wildlife Service, Region 1. Portland, Oregon.USFWS. 2008. Distribution of proposed critical habitat for the Marbled Murrelet (Brachyramphusmarmoratus) from the 1996 and 2008 designations. U.S. Fish and Wildlife Service, Pacific Region WWFWO GIS.

Midford, P.E., J.P. Hailman, and G.E. Woolfenden. 2000. Social learning of a novel foraging patch in families of free-living Florida scrub-jays. Animal Behaviour 59: 1199-1207.

Peery, M.Z., and R.W. Henry. 2010. Recovering marbled murrelets via corvid management: a population viability analysis approach. Biological Conservation 143:2414-2424.

Rockwell, C., P.O. Gabriel, and J.M. Black. 2012. Bolder, older, and selective: factors of individual-specific foraging behavior in Steller’s jays. Behavioral Ecology 23: 676-683.

Rockwell, C., P.O. Gabriel., and J.M. Black. 2013. Foraging dynamics in Steller’s jays: size and viability of cacheable food items. Animal Behaviour 86: 783-789.

Suddjian, D.L. 2009. Summary of 2008 – corvid monitoring surveys in the Santa Cruz mountains. Command Oil Spill Trustee Council, California Department of Fish and Game, Office for Oil Spill Prevention and Response, Sacramento, CA.

Templeton, J.J., A.C. Kamil, and R.P. Balda. 1999. Sociality and social learning in two species of corvids: The pinyon jay (Gymnorhinus cyanocephalus) and the Clark’s nutcracker (Nucifraga Columbiana). Journal of Comparative Psychology 113: 450-455.

USFWS. 2008. Distribution of proposed critical habitat for the Marbled Murrelet (Brachyramphusmarmoratus) from the 1996 and 2008 designations. U.S. Fish and Wildlife Service, Pacific Region WWFWO GIS Map. July 28, 2008.

# Text boxes

(b)

(a)

(a)

(b)

(e)

(a)											       (b)

(c)											      (d)

(b)

28         466                       29          453                       13         365

351         143                      343        139                       253       125